## Slide 1: Use of crop-soil-atmosphere dynamic models for (sub-)optimal irrigation management Raphael Linker
Associate Professor
Division of Environmental, Water and Agricultural Engineering
Faculty of Civil and Environmental Engineering
Technion – Israel Institute of Technology
Haifa

## Slide 2: Model-based (sub-) optimal irrigation scheduling (single crop)
Initial conditions
Weather
Soil characteristics
Dynamic model
Crop development
/yield
Irrigation
Crop parameters
Optimization tool
Prices
Quotas
Operational constraints
Objective
W,I,p)

## Slide 3: Model-based (sub-) optimal irrigation scheduling (single crop)
The optimization can be performed efficiently by defining as decision variables irrigation thresholds at which irrigation is triggered
What to optimize? Maximize yield; marginal yield; water use efficiency; profit; …?

## Slide 4: Model-based (sub-) optimal irrigation scheduling (single crop)
The optimization can be performed efficiently by defining as decision variables irrigation thresholds at which irrigation is triggered
What to optimize? Multi-objective optimization: Maximize yield and minimize irrigation
Find (t1, t2, … tn (,w1, w2, … wn))
such that
(-yield, total irrigation) minimum

## Slide 5: Model-based (sub-) optimal irrigation scheduling (single crop)
What to optimize? Multi-objective optimization: Maximize yield and minimize irrigation
t1, t2, …, tn
Irrigation on days
10
25
30
…

## Slide 6: Model-based (sub-) optimal irrigation scheduling (single crop)
What to optimize? Multi-objective optimization: Maximize yield and minimize irrigation
Quadratic approximation: Y*=f(I*)

## Slide 7: Model-based (sub-) optimal irrigation scheduling (single crop)
The optimization can be repeated during the season to account for the imperfectness of the weather forecasts

## Slide 8: Extensions:
Optimal allocation of land and/or water between several crops
Delineation of management zones (drip irrigation)

## Slide 9: Formalism for optimal crop selection and water allocation
Assumptions:
n crops
m fields (soil areas)
Weather forecasts/historical weather
Prices for crops (pi) and water (pw)
Operational constrains (water quotas, minimal yield, …)
n*m water productivity functions (Y*i,j(wi,j)) determined by single-crop multi-objective optimization
Decision variables
ai,j : Area of soil j allocated to crop i
wi,j : Amount of water allocated to crop i cultivated on soil j

## Slide 10: Formalism for optimal water allocation (during season or if cropping areas are fixed a priori)
Assumptions:
n crops
m fields (soil areas)
Weather forecasts/historical weather
Prices for crops (pi) and water (pw)
Operational constrains (water quotas, minimal yield, …)
n*m water productivity functions (fi,j) determined by single-crop multi-objective optimization
Decision variables
wi,j : Amount of water allocated to crop i cultivated on soil j
Recomputed using actual past weather and irrigation

## Slide 11: Formalism for optimal delineation of drip irrigation management zones
Direction of drip lines

## Slide 12: Formalism for optimal delineation of drip irrigation management zones
Direction of drip lines

## Slide 13: Formalism for optimal delineation of drip irrigation management zones

## Slide 14: On-going work/Open issues
Stochastic optimization to deal with weather forecasts uncertainty
Data assimilation (use of in-season measurements to improve model predictions)

## Slide 15: Stochastic optimization (Ensemble of Ns weather forecasts)
Implicit approach: Each forecast is used to solve a deterministic problem (independently) and some heuristic is used to select “the best” solution
Explicit one-stage approach: The optimization problems associated with the various forecasts are solved simultaneously, imposing the same set of optimal decisions for all forecasts:
Explicit two-stage approach: The optimization problems associated with the various forecasts are solved simultaneously, imposing that the first decision be the same for all forecasts:

## Slide 16: Stochastic optimization – Proposed scheme for multi-objective optimization inspired from “Explicit two-stage” approach

## Slide 17: Stochastic optimization – Proposed scheme for multi-objective optimization inspired from “Explicit two-stage” approach
 | Water Use Efficiency |  |  |  |  | 
Weather used to determine threshold of Period 3 | Weather used to determine thresholds of Periods 4-6 |  |  |  |  | 
 | 1965 | 1966 | 1967 | 1968 | 1969 | 
1965 | 0.0781 | 0.0493 | 0.1632 | 0.0589 | 0.0756 | 

## Slide 18: Stochastic optimization – Proposed scheme for multi-objective optimization inspired from “Explicit two-stage” approach

## Slide 19: Stochastic optimization – Proposed scheme for multi-objective optimization inspired from “Explicit two-stage” approach
 | Water Use Efficiency |  |  |  |  | 
Weather used to determine threshold of Period 3 | Weather used to determine thresholds of Periods 4-6 |  |  |  |  | 
 | 1965 | 1966 | 1967 | 1968 | 1969 | 
1965 | 0.0781 | 0.0493 | 0.1632 | 0.0589 | 0.0756 | 
1966 | 0.0781 | 0.0566 | 0.1631 | 0.0733 | 0.0760 | 
1967 | 0.0921 | 0.0531 | 0.1631 | 0.0668 | 0.0661 | 
1968 | 0.0668 | 0.0565 | 0.1614 | 0.0589 | 0.0662 | 
1969 | 0.0781 | 0.0565 | 0.2397 | 0.0667 | 0.0649 | 

## Slide 20: Stochastic optimization – Proposed scheme for multi-objective optimization inspired from “Explicit two-stage” approach
 | Water Use Efficiency |  |  |  |  | 
Weather used to determine threshold of Period 3 | Weather used to determine thresholds of Periods 4-6 |  |  |  |  | Median value
 | 1965 | 1966 | 1967 | 1968 | 1969 | 
1965 | 0.0781 | 0.0493 | 0.1632 | 0.0589 | 0.0756 | 0.0756
1966 | 0.0781 | 0.0566 | 0.1631 | 0.0733 | 0.0760 | 0.0773
1967 | 0.0921 | 0.0531 | 0.1631 | 0.0668 | 0.0661 | 0.0668
1968 | 0.0668 | 0.0565 | 0.1614 | 0.0589 | 0.0662 | 0.0662
1969 | 0.0781 | 0.0565 | 0.2397 | 0.0667 | 0.0649 | 0.0667

## Slide 21: Stochastic optimization – Proposed scheme for multi-objective optimization inspired from “Explicit two-stage” approach
Main open issues:
Which heuristic/metric should be used
Weight results according to forecasts probability

## Slide 22: Data assimilation:
Models are imperfect. Measurements are also imperfect. How to reconcile the two? Who should you believe (more)?
How to improve the “prediction power” of the model?

## Slide 23: Merci de votre attention Thank you תודה על ההקשבה